## Slide 1: SketchLib: Enabling Efficient Sketch-based Monitoring on Programmable Switches
Hun Namkung
Zaoxing Liu, Daehyeok Kim, Vyas Sekar, Peter Steenkiste

## Slide 2
Programmable Switches
Sketching Algorithms
Count-sketch
UnivMon (Sigcomm ‘16)
R-HHH (Sigcomm ’17)
… and much more!
Implementation should be easy?
Languages such as P4
Sketch seems promising on programmable switches

## Slide 3: Let’s try to run sketches on programmable switches
Programmable Switches
Sketching Algorithms
sketch.p4
Count-sketch
UnivMon (Sigcomm ‘16)
R-HHH (Sigcomm ’17)
Existing sketch code for CPU
(e.g., C++ / P4 code for BMv2)
Switch out of available resources

## Slide 4: Sketch is inefficient or infeasible on programmable switch
Programmable Switches
Sketching Algorithms
sketch.p4
Programmable switch has resource constraints (compiler rejects resource-heavy P4 code)
Difficult to program resource-efficient code for programmable switch
Existing sketch code for CPU
(e.g., C++ / P4 code for BMv2)
GAP

## Slide 5: Our work: SketchLib bridges the gap!
Programmable Switches
Sketching Algorithms
sketch.p4
API calls with resource optimization
SketchLib (https://github.com/SketchLib)
6 optimizations reduce resources up to 96% without accuracy degradation
Existing sketch code for CPU
(e.g., C++ / P4 code for BMv2)
API calls will automatically apply optimizations to P4 sketch codes
Identified four resource bottlenecks

## Slide 6: Outline
Bottleneck analysis
Optimizations and SketchLib APIs
Evaluation

## Slide 7: Two background questions for bottleneck analysis
Programmable Switches
Sketching Algorithms
sketch.p4
GAP
1. What are the common operations of sketches?
2. What are the hardware resources to run common operations of sketches?
Bottleneck Analysis

## Slide 8: Sketches have four common steps
Flowkey
Extraction
Hash
Computation
Memory Update
Tracking
Heavy Flowkey
Flowkey
Extraction
Hash
Computation
Memory Update
Tracking
Heavy Flowkey
Flowkey
Extraction
Hash
Computation
Counter Update
Tracking
Heavy Flowkey
Single-Level Sketch (e.g., count-sketch) vs Multi-Level Sketch (e.g., UnivMon)
192.168.0.1
Pkt header
flow definition
= srcIP
3
5
2
 |  | +1 |  | 
 |  |  |  | +1
 | +1 |  |  | 
Heap

## Slide 9: Sketch imposes burden on hardware resources
Programmable Switches
Flowkey
Extraction
Hash
Computation
Counter Update
Tracking
Heavy Flowkey
Parser
Stage 1
Stage N
Buffer
Stage 1
Stage N
…
…
Deparser
SRAM
SALU
Hash call
TCAM
Per-stage resource
Difficult to realize!
Bottleneck 3
Bottleneck 1
Bottleneck 2
Pipeline stages
Bottleneck 4

## Slide 10: Hash calls and SALUs are resource bottlenecks
Higher accuracy
Higher accuracy
[1] (UnivMon) Liu et al, One Sketch to Rule Them All: Rethinking Network Flow Monitoring with UnivMon (Sigcomm’ 16)
[2] (R-HHH) Basat et al, Constant Time Updates in Hierarchical Heavy Hitters (Sigcomm’ 17)

## Slide 11: Outline
Bottleneck analysis
Optimizations and SketchLib APIs
Evaluation

## Slide 12: Overview of optimizations and SketchLib API
Resource Bottlenecks | Optimizations | SketchLib API
Hash Calls | O1. Consolidate short-bit hash calls | hash_consolidate_and_split()
 | O2. Reuse hash calls across levels | select_key_and_hash()
Pipeline Stages | O3. Remove dependencies using TCAM | tcam_optimization()
SALUs | O4. Update only one level per packet | -
 | O5. Rewrite P4 code to reduce SALUs | consolidate_update()
Resources for tracking flowkeys | O6. Hash table for tracking heavy flowkeys | heavy_flowkey_storage()

## Slide 13: O1. Consolidate short hash calls
Hash Call
flowkey
seed
bit length
hash result
1-bit Hash Call
1-bit Hash Call
1-bit Hash Call
0
0
1
3 hash calls
0 1 0
3-bit Hash Call
1 hash call
Short (e.g., 1-bit)
[Condition] same flowkeys
Accuracy-preserving ✓

## Slide 14
9 SALUs
L=3
SALU
3 SALUs
SALU
SALU
SALU
SALU
SALU
SALU
SALU
SALU
SALU
SALU
SALU
O5. Remove unnecessary SALU allocation
✗
✗
✓
Accuracy-preserving ✓

## Slide 15
End-to-end code example
...
h1 = hash(srcIP, seed1, 1);
h2 = hash(srcIP, seed2, 1);
h3 = hash(srcIP, seed3, 1);
...
if (L == 1)
update_array_1(L, index);
if (L == 2)
update_array_2(L, index);
if (L == 3)
update_array_3(L, index);
...
UnivMon.p4 without SketchLib
SketchLib
O1: hash_consolidate_and_split()
O5: consolidate_update()
https://github.com/SketchLib
Optimized UnivMon.p4
...
hash_consolidate_and_split (
srcIP, seed1, 3, 1, 1, 1);
...
consolidate_update (L, index);
...

## Slide 16
# | Sketch Type | Sketch Name | Venue | Applicability of SketchLib
1 | Frequency Estimation / HeavyHitters | Count-Min Sketch | Journal of Algorithms ‘04 | O6
2 |  | Count Sketch | ICALP ‘02 | O1, O6
3 |  | MRAC | Sigmetrics ‘04 | O3, O5
4 | Hierarchical Heavy Hitters | RHHH | Sigcomm ‘17 | O1, O2, O5, O6
5 |  | HHH | VLDB ‘03 | O1, O6
6 | Cardinality | PCSA | JCSS ‘85 | O3, O5
7 |  | MRB | IMC ‘03 | O3, O5
8 |  | LogLog | ESA ‘03 | O3
9 |  | HyperLogLog | AOFA ‘07 | O3
10 | Entropy | EntropySketch | Sigmetrics ‘06 | O1
11 | Change detection | K-ary | IMC ‘03 | O1, O2, O6
12 | Super Spreader | SpreadSketch | Infocomm ‘20 | O3, O5
13 | General | UnivMon | Sigcomm ‘16 | O1, O2, O3, O4, O5, O6
14 |  | FCM | CoNEXT ‘20 | O6
15 |  | SketchLearn | Sigcomm ‘18 | O2
Applicability of SketchLib
https://github.com/SketchLib

## Slide 17: Outline
Bottleneck analysis
Optimizations and SketchLib API
Evaluation

## Slide 18
Chart: Sketches
| CS | HLL | UnivMon | RHHH | MRAC | MRB | PCSA
Hash Calls | 31 | 80 | 91 | 92 | 87 | 90 | 92
SALUs | 0 | 0 | 90 | 92 | 91 | 93 | 96
Pipeline Stages | 9 | 86 | 65 | 62 | 68 | 76 | 86
SketchLib reduces resource bottlenecks

## Slide 19
SW baseline
SketchLib-optimized on HW
Error (%)
SketchLib preserves accuracy

## Slide 20
The promise of sketch today is still unrealized
SketchLib helps developers optimize sketch implementations on programmable switches with minimal effort
SketchLib is general across sketches
https://github.com/SketchLib
Conclusion