## Slide 1: Telemetry Retrieval Inaccuracy in Programmable Switches Analysis and Recommendations
Hun Namkung§
Daehyeok Kim §† , Zaoxing Liu‡, Vyas Sekar§, Peter Steenkiste§
§Carnegie Mellon University
‡Boston University
†Microsoft Research

## Slide 2: Sketches on programmable switches are promising
Network Operator
Telemetry Result
Programmable Switch (Tbps)
Packet Stream
Sketches
Heavy hitter detection
Entropy estimation
Unique # of flows
Counter Arrays

## Slide 3: Sketches on programmable switches generate inaccurate results
 | Counter Array Size |  | 
 | 16K | 32K | 64K
Expected | 4.1% | 1.3% | 0.3%
Observed | 7.1% | 17.0% | 34.8%
94x more error!
Average Error Rate (%)
on count-min sketch
This inaccuracy problem also impacts other sketches!

## Slide 4: Counter retrieval causes the inaccuracy problem
time
Counter
Arrays
Packet
Stream
Data Plane
Switch
Control Plane
epoch1
update
epoch2
update
epoch3
update
This problem also impacts other telemetry tasks!
counter
retrieval
counter
retrieval

## Slide 5: Read/Reset delays can cause counting errors
Counter
Arrays
Packet
Stream
Data Plane
Switch
Control Plane
epoch1
update
epoch2
update
epoch3
update
read
reset
read
reset
read
reset
read
reset
time

## Slide 6: Read/Reset delays can cause counting errors
Counter
Arrays
Packet
Stream
Data Plane
Switch
Control Plane
epoch1
update
epoch2
update
epoch3
update
read
reset
reset
reset
read
read
read
Undercounting!
time

## Slide 7: Read/Reset delays can cause counting errors
Counter
Arrays
Packet
Stream
Data Plane
Switch
Control Plane
epoch1
update
read
reset
epoch2
update
read
reset
epoch3
update
read
reset
time
Overcounting!
Undercounting!

## Slide 8: Analysis reveals two major bottlenecks
Counter
Arrays
Counter
Arrays
62%
36%
Delay contributing to undercounting (99.9%)
Delay contributing to overcounting (1%)
100%

## Slide 9: Sol 1. Use two sets of counter arrays
Set 2
epoch1
epoch2
epoch3
Packet
Stream
Data Plane
Switch
Control Plane
Set 1
update
update
update
read reset
read reset

## Slide 10: Sol 2. No reset operation
Counter
Arrays
Packet
Stream
Data Plane
Switch
Control Plane
epoch1
update
read
reset
epoch2
update
read
reset
epoch3
update
read
reset
…
…
Linear property enables

## Slide 11: Trade-offs among independent solutions and guideline
 | Generality | Delay Reduction | Memory Efficiency
Sol 1. Use two sets of counter arrays | ✓ | 100% | ✗
Sol 2. No reset operation | ✗ | 99% | ✓
Sol 3. Defer buffer read and perform bulk reset | ✓ | 95% | ✓
(Higher is better)
Resources is sufficient and/or high accuracy is required?
Sol 1
yes
no
Sketch satisfies the linear property?
yes
Sol 2
no
Sol 3

## Slide 12: Evaluation Setup
Tofino Programmable Switch
Control Plane
Data Plane
Server
tcpreplay
CAIDA traces
periodically read and reset
Sketches
Multi-Resolution Bitmap
HyperLogLog
Count-min Sketch
Count-Sketch
UnivMon

## Slide 13: Accuracy Improvement
Lower is better
Chart: Five Sketches
| Multi-resolution Bitmap | HyperLogLog | CountSketch | CountMin | UnivMon
Expected | 1.6 | 4.8 | 0.7 | 0.4 | 2.8
Unoptimized | 20.1 | 6.2 | 35.4 | 34.8 | 64.7
Sol 1 | 1.6 | 4.8 | 0.7 | 0.4 | 2.8
Sol 2 | 0 | 0 | 1 | 0.7 | 2.8
Sol 3 | 1.7 | 4.8 | 1.5 | 1.1 | 3.6

## Slide 14: Conclusion
Control plane counter retrieval problem generate inaccurate results for sketches on the programmable switch.
Our work:
We analyze and quantify the inaccuracy
We propose three solutions and they eliminate almost all the inaccuracy